SSN 1392-3196

Žemdirbystė=Agriculture, vol. 99, No. 4 (2012), p. 371–378

UDK  633.15:631.348.45

## The effects of drift-reducing nozzles on herbicide efficacy             and maize (Zea mays L.) yield

##### Mario LEŠNIK, Branko KRAMBERGER, Stanislav VAJS

# University of Maribor, Faculty of Agriculture and Life Sciences

# Pivola 10, SI-2311 Hoče, Slovenia

# E-mail: mario.lesnik@uni-mb.si

###### Abstract

Field trials were carried out in 2009–2011 to compare the performance of herbicides for weed control in maize (Zea mays L.). Herbicides were applied by standard (API, “Albuz”) and by drift-reducing (AVI, “Albuz”) nozzles. Mixtures of herbicides based on 2,4-D, bentazon and foramsulfuron were applied post-emergence with a tractor mounted field boom sprayer at a spray volume of 150 or 300 l ha-1 in the form of droplets of different size classes (volume median diameter (VMD) from 100 to 800 µm). The main weed species in the field trials were: Ambrosia artemisiifolia, Amaranthus retroflexus, Chenopodium album, Convolvulus arvensis, Elytrigia repens, Echinochloa crus-galii, Polygonum lapathifolium and Fallopia convolvulus. The efficacy (%) of herbicides  and maize yield were assessed. The impact of the studied factors on herbicide efficacy against broad-leaved weed species differed from that against narrow-leaved species. In comparison to the standard API nozzles, the overall efficacy of drift-reducing AVI nozzles was lower in 8 of 12 herbicide applications. The efficacy reduction ranged from 2% to 7%. The type of nozzle had a significant influence on the yield of maize cobs in 5 of 12 herbicide applications, and spray volume significantly affected maize cob yield in 7 of 12 herbicide applications. In all statistically significant cases, maize yield was higher when herbicides had been applied by standard nozzles (API, VMD 100–300 µm) at 300 l ha-1 spray volume. The highest yield reductions due to the use of AVI nozzles (7–11%) were determined in the case of low volume sprays (150 l ha-1) consisting of big droplets (VMD more than 400 µm). Results suggest that AVI nozzles can cause poor weed control only if used for applications of small spray volumes (less than 200 l ha-1) with droplet VMD values larger than 400 µm, otherwise weed control results comparable to standard API nozzles are achieved and the use of drift-reduction AVI nozzles does not result in maize yield reduction.

Key words: drift-reducing nozzles, Zea mays, weed control, 2,4-D, bentazon, foramsulfuron.

ISSN 1392-3196

Žemdirbystė=Agriculture, vol. 99, No. 4 (2012), p. 371–378

UDK  633.15:631.348.45

### Purkštukų tipo įtaka herbicidų efektyvumui ir paprastojo kukurūzo (Zea mays L.) derliui

##### M. Lešnik, B. Kramberger, S. Vajs

# Maribor universitetas, Slovėnija

###### Santrauka

Siekiant palyginti herbicidų efektyvumą paprastojo kukurūzo (Zea mays L.) pasėliui, lauko bandymai vykdyti 2009–2011 m. Herbicidai purkšti standartiniais (API, “Albuz”) ir specialiais (AVI, “Albuz”) purkštukais, mažinančiais lašelių nunešimą pavėjui. Herbicidų mišiniai, sudaryti iš 2,4-D, bentazono ir foramsulfurono, purkšti pasėliui sudygus, naudojant pakabinamą lauko purkštuvą, 150 ir 300 l tirpalo hektarui. Išpurškiamo tirpalo lašeliai skyrėsi dydžiu, jų tūrio medianinis skersmuo buvo nuo 100 iki 800 µm. Bandymų pagrindinės piktžolių rūšys buvo Ambrosia artemisiifolia, Amaranthus retroflexus, Chenopodium album, Convolvulus arvensis, Elytrigia repens, Echinochloa crus-galii, Polygonum lapathifolium ir Fallopia convolvulus. Vertintas herbicidų efektyvumas (%) ir kukurūzų derlius. Nustatyta skirtinga tirtų veiksnių įtaka herbicidų efektyvumui plačialapėms ir siauralapėms piktžolėms. Palyginus su standartiniais API purkštukais, AVI purkštukų, mažinančių lašelių nunešimą pavėjui, efektyvumas buvo mažesnis 8 iš 12 herbicidų purškimo atvejų. Efektyvumo sumažėjimas svyravo nuo 2 iki 7 %. Kukurūzų burbuolių derliui reikšmingą įtaką purkštuko tipas turėjo 5 iš 12, o purškiamo tirpalo norma – 7 iš 12 herbicidų purškimo atvejų. Visais atvejais kukurūzų derlius iš esmės didesnis buvo herbicidus išpurškus standartiniais purkštukais (API, tūrio medianinis skersmuo – 100–300 µm), 300 l ha-1 tirpalo. Didžiausias derliaus sumažėjimas (7–11 %) naudojant AVI purkštukus nustatytas purškiant mažą (150 l ha-1) normą dideliais lašeliais (tūrio medianinis skersmuo didesnis nei 400 µm). Tyrimo rezultatai parodė, kad purškiant AVI purkštukais gaunama prasta piktžolių kontrolė, jeigu purškiama maža (mažiau nei 200 l ha-1) norma tirpalo, tūrio medianinio skersmens vertėms esant didesnėms nei 400 µm. Kitais atvejais piktžolių kontrolė yra panaši į gaunamą naudojant API purkštukus, o AVI purkštukų, mažinančių lašelių nunešimą pavėjui, naudojimas kukurūzų derliaus nesumažina.

Reikšminiai žodžiai: purkštukai, mažinantys lašelių nunešimą pavėjui, Zea mays, piktžolių kontrolė, 2,4-D, bentazonas, foramsulfuronas.